## Slide 1: Mission Planner Advanced Features and Hardware-in-the-Loop Simulation
2/9/15
Melanie Clark

## Slide 2: Mission Planner Advanced Features
Google Earth Logging
Each flight automatically logged, saved as .tlog in “logs” subfolder of Mission Planner
Telem. uplink rates adjustable in MP ->Config/Tuning>Planner

## Slide 3: Mission Planner Advanced Features
Google Earth Logging
Flight modes viewed individually
Lat/Long, Altitude/Pitch/Roll/Yaw data available for each point.
First-person view replay available

## Slide 4: Mission Planner Advanced Features
Mission Planning
Point-and-click flight paths
  Takeoff, WP, loiter, RTL, land & more
Loiter options: forever, # circles, specific time
New mission can be programmed and uploaded via telemetry during active mission

## Slide 5: Mission Planner Advanced Features
Other Mission Planning Features of Interest (from drop-down menus)
Condition_Delay
  Delays execution of next command
Do_Set_ROI
  Points nose of vehicle and camera gimbal to the programmed “region of interest”
Do_Jump
  Jumps to specific WP specific # of times. (Useable only 3 times per mission)
Do_Change_Speed
Do_Set_Cam_Trigg_Dist
  Triggers the camera shutter at regular distance intervals

## Slide 6: Mission Planner Advanced Features
RTL: Return to Launch
Returns plane to launch point (where GPS lock first established)
Plane will rise to RTL_ALT as it returns home
Important to acquire GPS lock before arming for any GPS dependent mode to work properly.
Flight Modes
Flight modes assigned to transmitter switches in MP ->Initial Setup -> Flight Modes
When switched to Auto (Programmed Mission), plane continues from previous mission item
While in Auto, pilot has partial control of plane via “stick mixing,” similar to FBWA mode

## Slide 7: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane

## Slide 8: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane
APM connected to computer by USB but not “Connected” to Mission Planner
In Mission Planner Initial Setup -> HIL Simulator -> Plane
MP serves as bridge to X-Plane and sends output from APM to flight simulator
X-Plane and MP can run on separate computers, as they communicate over network (important for improved framerate)

## Slide 9: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane
In X-Plane: Settings -> Data Input & Output

## Slide 10: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane
In X-Plane: Settings -> Net Connection
Enter IP of computer running MP
IP in image is loopback

## Slide 11: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane
Check X-Plane box
Enter IP of computer running X-Plane (port 49000)
Select Sim Link Start/Stop
To test: set three RC toggle switch modes to Manual, Stabalize and RTL via MAVLink (ctrl-G)

## Slide 12: Mission Planner Advanced Features
Hardware-in-the-Loop Simulation With X-Plane
Once flying in sim, hit ‘C’ to view plane
Verify transmitter sticks move control surfaces in correct direction
  Reversal is done as normal RC control
Enjoy your flight!